## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-6)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Final Term Lecture - 05

## Slide 2: TRANSFER CURVE
To determine ID given VGS:
where VT = threshold voltage or voltage at which the MOSFET turns on.
k = constant found in the specification sheet
k can also be determined by using values at a specific point and the formula:
VDSsat can also be calculated:

## Slide 3: P -CHANNEL ENHANCEMENT-TYPE MOSFETS
The p-channel Enhancement-type MOSFET is similar to the n-channel except that the voltage polarities and current directions are reversed.

## Slide 4: SYMBOLS

## Slide 5: DEPLETION-TYPE MOSFET CONSTRUCTION
The Drain (D) and Source (S) connect to the to n-doped regions.
These N-doped regions are connected via an n-channel. This n-channel is connected to the Gate (G) via a thin insulating layer of SiO2.
The n-doped material lies on a p-doped substrate that may have an additional terminal connection called SS.

## Slide 6: BASIC OPERATION
In Fig. 6.25 the gate-to-source voltage is set to 0 V by the direct connection from one terminal to the other, and a voltage VDD is applied across the drain-to-source terminals.
The result is an attraction of the free electrons of the n-channel for the positive voltage at the drain.
The result is a current similar to that flowing in the channel of the JFET. In fact, the resulting current with VGS = 0 V continues to be labeled IDSS.

## Slide 7: BASIC OPERATION
A Depletion MOSFET can operate in two modes: Depletion or Enhancement mode.

## Slide 8: BASIC OPERATION CONTD.
In this figure VGS has been set at a negative voltage such as 1 V. The negative potential at the gate will tend to pressure electrons toward the p-type substrate (like charges repel) and attract holes from the p-type substrate (opposite charges attract).
Depending on the magnitude of the negative bias established by VGS, a level of recombination between electrons and holes will occur that will reduce the number of free electrons in the n-channel available for conduction. The more negative the bias, the higher the rate of recombination.
The resulting level of drain current is therefore reduced with increasing negative bias for VGS for VGS =1 V, 2 V, and so on, to the pinch-off level of 6 V. The resulting levels of drain current and the plotting of the transfer curve proceeds exactly as described for the JFET.

## Slide 9: DEPLETION-TYPE MOSFET IN DEPLETION MODE
Depletion mode:
The characteristics are similar to the JFET.
When VGS = 0V, ID = IDSS
When VGS < 0V, ID < IDSS
The formula used to plot the Transfer Curve still applies:

## Slide 10: ENHANCEMENT MODE
For positive values of VGS, the positive gate will draw additional electrons (free carriers) from the p-type substrate due to the reverse leakage current and establish new carriers through the collisions resulting between accelerating particles.
As the gate-to-source voltage continues to increase in the positive direction, the drain current will increase at a rapid rate.
The application of a positive gate-to-source voltage has “enhanced” the level of free carriers in the channel compared to that encountered with VGS =0 V. For this reason the region of positive gate voltages on the drain or transfer characteristics is often referred to as the enhancement region,
The region between cutoff and the saturation level of IDSS referred to as the depletion region.

## Slide 11: DEPLETION-TYPE MOSFET IN ENHANCEMENT MODE
Enhancement mode:
VGS > 0V, ID increases above IDSS.
The formula used to plot the Transfer Curve still applies:
(note that VGS is now a positive polarity)

## Slide 12: P-CHANNEL DEPLETION-TYPE MOSFET
The p-channel Depletion-type MOSFET is similar to the n-channel except that the voltage polarities and current directions are reversed.

## Slide 13: SYMBOLS

## Slide 14: SUMMARY TABLE

## Slide 15: MOSFET HANDLING
MOSFETs are very static sensitive. Because of the very thin SiO2 layer between the external terminals and the layers of the device, any small electrical discharge can stablish an unwanted conduction.
Protection:
    Always transport in a static sensitive bag.
    Always wear a static strap when handling MOSFETS.
    Apply voltage limiting devices between the Gate and Source, such as back-to-back Zeners to limit any transient voltage.

## Slide 16: CMOS
CMOS – Complementary MOSFET p-channel and n-channel MOSFET on the same substrate.
Advantage:
    Useful in logic circuit designs
    Higher input impedance
    Faster switching speeds
    Lower operating power levels
Application:
    CMOS Inverter

## Slide 17: CMOS INVERTER
An inverter is a logic element that “inverts” the applied signal. That is, if the logic levels of operation are 0V (0-state) and 5V (1-state), an input level of 0V will result in an output level of 5V, and vice versa.
Here, both gates are connected to the applied signal and both drain to the output Vo. The source of the p-channel MOSFET (Q2) is connected directly to the applied voltage VSS, while the source of the n-channel MOSFET (Q1) is connected to ground.
Here, the application of 5V at the input should result in approximately 0 V at the output. With 5V at Vi (with respect to ground), VGS1 = Vi and Q1 is “on,” resulting in a relatively low resistance between drain and source.
Since Vi and VSS are at 5 V, VGS2 = 0 V, which is less than the required VT for the device, resulting in an “off” state. The resulting resistance level between drain and source is quite high for Q2.

## Slide 18: CMOS INVERTER
A simple application of the voltage-divider rule will reveal that Vo is very close to 0 V or the 0-state, establishing the desired inversion process.
For an applied voltage Vi of 0V (0-state), VGS1 = 0V and Q1 will be off with VSS2 =-5V, turning on the p-channel MOSFET. The result is that Q2 will present a small resistance level, Q1 a high resistance, and Vo =VSS =5 V (the 1-state).

## Slide 19
End of Lecture-5